## Slide 1: NegotiaToR: Towards A Simple Yet Effective On-demand Reconfigurable Datacenter Network
Cong Liang1, Xiangli Song1, Jing Cheng1, Mowei Wang2, Yashe Liu2, Zhenhua Liu2, Shizhen Zhao3, Yong Cui1
1Tsinghua University, 2Huawei Technologies Co., Ltd, 3Shanghai Jiao Tong University

## Slide 2
Background: Optical switching in DCN
Electrical packet switching: Capacity limitation in the post Moore’s Law era
Optical switching: High capacity & Low cost
  Recent advance of AWGR-based switching hardware
    Low end-to-end reconfiguration delay: Within 10 ns[1]
    DCN scalability: Using flat topologies above ToRs
Sufficient for fast reaction to dynamic traffic patterns among ToRs
[1] Ballani et al., SIGCOMM ’20
  But how to schedule the fast-reconfigurable optical links?
src ToR
dst ToR
AWGR
  Thin-clos topology
  (Low port-count AWGRs)
  Parallel network topology
  (High port-count AWGRs)
AWGR
ToR

## Slide 3
Scheduling the fast-reconfigurable optical links among ToRs
[1] Ballani et al., SIGCOMM ’20
  Practical yet high performance on-demand distributed scheduling?
Goal: Rapidly getting non-conflicting paths
Traffic-oblivious: Predefined uniform round-robin & Data relay (e.g., Sirius[1])
  Practical scheduler-less design
  Topology & traffic mismatch: Sacrificed latency and goodput
On-demand: Adapting topology to real-time traffic demands
  Potentially better performance
  Practicality concerns: Fast on-demand distributed scheduling?

## Slide 4
flow to A @ t1, size U
flow to B @ t2, size V
flow to C @ t3, size W
…
flow from D @ t4, size X
flow from E @ t5, size Y
flow from F @ t6, size Z
…
Y > Z > X
t6 > t5 > t4
measurement
calculation
Challenges: On-demand distributed scheduling of
fast-reconfigurable optical links among ToRs
Demand measurement + Fast calculation at DCN scale?
  Challenge 1: High implementation complexity
dynamic demands among ToRs
Src
ToR
Dst
ToR

## Slide 5
Demand measurement + Fast calculation at DCN scale?
  Challenge 1: High implementation complexity
Separate network for scheduling messages?
  Challenge 2: Expensive to build and maintain a separate control plane
Src
ToR
Dst
ToR
dynamic demands
decisions
Challenges: On-demand distributed scheduling of
fast-reconfigurable optical links among ToRs

## Slide 6
Src
ToR
Dst
ToR
dynamic demands
decisions
Demand measurement + Fast calculation at DCN scale?
  Challenge 1: High implementation complexity
Separate network for scheduling messages?
  Challenge 2: Expensive to build and maintain a separate control plane
Scheduling delay vs. Mice flows / Incasts?
  Challenge 3: Downgraded latency due to scheduling delay
Challenges: On-demand distributed scheduling of
fast-reconfigurable optical links among ToRs

## Slide 7
An on-demand reconfigurable DCN architecture towards a simple yet effective design
Challenge 1
High implementation complexity
Challenge 3
Downgraded latency
due to scheduling delay
Challenge 2
Expensive to build and maintain
a separate control plane
NegotiaToR overview
NegotiaToR Matching algorithm
Towards minimalist on-demand scheduling on flat topologies
Two-phase epoch
In-band pipelined scheduling & One-hop direct transmission
Scheduling delay bypassing
FCT optimization for latency-sensitive flows

## Slide 8: Scheduling optical links among ToRs on flat topologies
Conflicts at ports:
Similar problems exist in crossbar packet switches
  Non-conflicting input-output matches: PIM[1], RRM[2], iSLIP[3]…
    Fast and practical
    Extensive implementation experience
Many-to-one
One-to-many
Flat topology
A matching problem!
NegotiaToR Matching (inspired by RRM[2])
[1] Anderson et al., ToCS ’93
[2] McKeown, PhD Thesis, UC
Berkeley ’95
[3] McKeown et al., ToN ’99
input
output
input
output

## Slide 9
AWGR
Src
Dst
Example on the parallel network topology:
NegotiaToR Matching on flat topologies

## Slide 10
AWGR
to ToR 2
to ToR 2, 4
Traffic
demands
Src
Dst
Example on the parallel network topology:
Each port can receive from all other ToRs
Need to schedule multiple ports simultaneously
_
NegotiaToR Matching on flat topologies

## Slide 11
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
Example on the parallel network topology:
NegotiaToR Matching on flat topologies

## Slide 12
Src
Dst
Traffic
demands
from ToR 1, 3
to ToR 2
to ToR 2, 4
CONFLICT
from ToR 3
Example on the parallel network topology:
binary request
binary request
binary request
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations

## Slide 13
Src
Dst
Traffic
demands
from ToR 1, 3
to ToR 2
to ToR 2, 4
CONFLICT
1
3
1
2
3
4
5
6
8
7
ToR 2’s
GRANT ring
from ToR 3
Example on the parallel network topology:
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM

## Slide 14
1
3
1
2
3
4
5
6
8
7
ToR 2’s
GRANT ring
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
for ToR 1
for ToR 3
for ToR 1
for ToR 3
from ToR 3
Example on the parallel network topology:
Ports share one ring for fairness
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM

## Slide 15
3
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
1
3
1
2
3
4
5
6
8
7
ToR 4’s
GRANT ring
for ToR 1
for ToR 3
for ToR 1
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 3
1
3
1
2
3
4
5
6
8
7
ToR 2’s
GRANT ring
Example on the parallel network topology:
Ports share one ring for fairness
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM

## Slide 16
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
for ToR 1
for ToR 3
for ToR 1
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 1
for ToR 3
for ToR 1
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 3
Example on the parallel network topology:
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM

## Slide 17
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
for ToR 1
for ToR 3
for ToR 1
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 3
to ToR 2, 4
to ToR 2
to ToR 2, 4
to ToR 2
to ToR 4
to ToR 4
for ToR 1
for ToR 3
for ToR 1
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 3
CONFLICT
Example on the parallel network topology:
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM

## Slide 18
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
for ToR 1
for ToR 3
for ToR 1
for ToR 3
for ToR 3
for ToR 3
for ToR 3
for ToR 3
to ToR 2, 4
to ToR 2
to ToR 2, 4
to ToR 2
to ToR 4
to ToR 4
per-port ACCEPT ring
Example on the parallel network topology:
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM
Port-level ACCEPT
Eliminate one-to-many conflicts at sources with RRM

## Slide 19
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
to ToR 2, 4
to ToR 2
to ToR 2, 4
to ToR 2
to ToR 4
to ToR 4
per-port ACCEPT ring
✓
✓
✓
✓
✓
✓
Example on the parallel network topology:
NegotiaToR Matching on flat topologies
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM
Port-level ACCEPT
Eliminate one-to-many conflicts at sources with RRM

## Slide 20
ToR-level REQUEST
Send binary requests to destinations
Port-level GRANT
Eliminate many-to-one conflicts at destinations with RRM
Src
Dst
Traffic
demands
to ToR 2
to ToR 2, 4
Port-level ACCEPT
Eliminate one-to-many conflicts at sources with RRM
Example on the parallel network topology:
Wavelength tuning according to locally derived scheduling results
NegotiaToR Matching on flat topologies

## Slide 21: Adapting NegotiaToR Matching to topology capability
AWGR
Src
Dst
For topologies with limited connectivity…
  Example on the thin-clos topology with lower port-count AWGRs

## Slide 22: Adapting NegotiaToR Matching to topology capability
AWGR
Src
Dst
For topologies with limited connectivity…
  Example on the thin-clos topology with lower port-count AWGRs
1
3
1
2
3
4
5
6
8
7
Each port can only receive from a subset of ToRs
8
7
5
6
4
3
2
1
per-port GRANT rings
Modify the rings to match the topology’s capability

## Slide 23
Intuitive
solution
time
ToR-level REQUEST
Port-level GRANT
Port-level ACCEPT
Supporting frequent exchanges of scheduling messages
Requires full-mesh connectivity among all ToRs
Following previous practices[1][2][3]
  Round-robin reconfiguration to work as full-mesh
One-way delay (μs) between ToRs (at least)
One-way delay (μs) between ToRs (at least)
Link waste due to long one-way delay
[1] Mellette et al., SIGCOMM ’17
[2] Shrivastav et al., NSDI ’19
[3] Ballani et al., SIGCOMM ’20
reconfiguration delay
scheduling messages
data

## Slide 24
Pipelined scheduling through two-phase epochs
requestn
grantn
acceptn
Pipelined scheduling: Run three scheduling processes simultaneously
  Get a set of accepts after each round-robin
  Reconfiguration and data transmission after accepts
grantn-1
acceptn-2
requestn+1
acceptn-1
grantn+1
requestn+2
reconfiguration delay
scheduling messages
data

## Slide 25
Pipelined scheduling through two-phase epochs
Predefined phase
Frequent reconfigurations
Predefined connections
Pipelined distributed scheduling
reconfiguration delay
scheduling messages
data
Scheduled phase
No reconfiguration during it
On-demand connections
Send data through direct paths
One NegotiaToR Epoch (fixed time interval)

## Slide 26
Latency vs. Scheduling delay
Bypassing scheduling delay to optimize latency?
Mice flows? Incasts?
Long scheduling delay (even in lucky cases)
Due to μs one-way delay between ToRs
The scheduling delay may be longer when conflicts occur
2 epochs
acceptn
grantn
requestn
no traffic
new traffic
grantn-1
acceptn-2
requestn+1
acceptn-1
grantn+1
requestn+2
Epoch n
Epoch n+1
Epoch n+2
reconfiguration delay
scheduling messages
data
time

## Slide 27
Scheduling delay bypassing for latency optimization
acceptn
grantn
requestn
no traffic
new traffic
grantn-1
acceptn-2
requestn+1
acceptn-1
grantn+1
requestn+2
Epoch n
Epoch n+1
Epoch n+2
reconfiguration delay
scheduling messages
data
Predefined phase:
Full-mesh connectivity
Control plane: Exchanges of scheduling messages
Role of the predefined phase
time

## Slide 28
acceptn
grantn
requestn
no traffic
new traffic
grantn-1
acceptn-2
requestn+1
acceptn-1
grantn+1
requestn+2
Data plane: Also piggybacking small data packets
  Guaranteed unscheduled transmission
  Sufficient for mice flows (small in size), even under incasts
Epoch n
Epoch n+1
Epoch n+2
reconfiguration delay
scheduling messages
data
Control plane: Exchanges of scheduling messages
Predefined phase:
Full-mesh connectivity
Role of the predefined phase
Scheduling delay bypassing for latency optimization
time

## Slide 29
  Maximize opportunities: Prioritize mice flows
    Information-agnostic mice flow prioritization like PIAS[1]
HoL blocking by elephant flows?
[1] Bai et al., NSDI ’15
acceptn
grantn
requestn
no traffic
new traffic
grantn-1
acceptn-2
requestn+1
acceptn-1
grantn+1
requestn+2
Epoch n
Epoch n+1
Epoch n+2
reconfiguration delay
scheduling messages
data
Predefined phase:
Full-mesh connectivity
Control plane: Exchanges of scheduling messages
Data plane: Also piggybacking small data packets
  Guaranteed unscheduled transmission
  Sufficient for mice flows (small in size), even under incasts
Role of the predefined phase
Scheduling delay bypassing for latency optimization
time

## Slide 30
NegotiaToR’s design efforts towards practicality
Proven implementation strategies
  Inspired by RRM[1]: Programmable priority encoders to implement rings[2]
Simple designs
  No iteration
  No data relay
  Binary requests
  Stateless scheduling
[1] McKeown, PhD Thesis, UC
Berkeley ’95
[2] Gupta et al., IEEE Micro ’99
Could a more complex design significantly improve NegotiaToR’s performance?

## Slide 31
Possibly downgraded performance (Confirmed by experimental results)
Example: Iterative scheduling?
  Following practices in crossbar switch port matching
  Difference: NegotiaToR has a longer delay between consecutive steps
The rationality of NegotiaToR’s design choices
No iteration
3 iterations
Scheduling delay: 6 epochs +
Scheduling delay: 2 epochs +
Outdated requests
Link waste
Please refer to our paper for more explorations
μs one-way delay between ToRs
data may already be sent…

## Slide 32
Evaluation
99th-percentile FCT of mice flows (<10KB)
Goodput
[1] Roy et al., SIGCOMM ’15
[2] Ballani et al., SIGCOMM ’20
Simulation setup: 128 ToRs, Hadoop trace[1]
  Connected by 2 flat topologies
  10 ns reconfiguration delay
  2x speedup for both NegotiaToR
  and the traffic-oblivious scheme[2]
  Consider ToRs as endpoints
  Results without mice flow
  prioritization are also shown
NegotiaToR achieves both small mice flow FCT and high goodput
on two representative flat topologies

## Slide 33
An on-demand reconfigurable DCN architecture towards a simple yet effective design
NegotiaToR summary
NegotiaToR Matching algorithm
Towards minimalist on-demand scheduling
on flat topologies
Two-phase epoch
In-band pipelined scheduling &
One-hop direct transmission
Scheduling delay bypassing
FCT optimization for
latency-sensitive flows
Thank you!
Speaker: Cong Liang
liangxcong@outlook.com